# 09 5113 	ACOUSTICAL PANEL CEILINGS

FINAL:  	Feb. 12, 2009

Note:  The following specification criteria have been assembled to promote the procurement of post-consumer/post-industrial recycled content in mineral wool and cellulose fiber based acoustical ceiling panels and their steel suspension systems. Additional considerations related to product emissions, product toxicity, or other High Performance building criteria are included where appropriate.

PART 1 - GENERAL

1.01  SUMMARY

- This section includes mineral wool and cellulose fiber based acoustical panel ceiling systems which meet specified criteria for:

- Post consumer and/or post industrial recycled content in the ceiling panels; and

- Post consumer and/or post industrial recycled content in the ceiling suspension system

  - REFERENCES / QUALITY ASSURANCE

(for recycled content and other High Performance building criteria)

- Recycled Content (Steel Suspension Systems):

Steel Recycling Institute, 1740 Massachusetts Avenue, Boxborough MA 01719,

978-266-1847, www.recycle-steel.org/

1.03	SUBMISSION REQUIREMENTS

A	Manufacturer’s certification of recycled content per section 2.01 of this specification.

- Manufacturer’s certification of product compliance with emissions testing standards per section 2.01 of this specification.

- Material Safety Data Sheets.

- Manufacturer’s maintenance and cleaning instructions.

- Manufacturer’s policy statement on ceiling panel /ceiling suspension system recycling programs.

1.04	DELIVERY AND STORAGE

- Where feasible, remove acoustical ceiling panels from packaging and store in unoccupied, ventilated areas (100% outside air supply, minimum of 1.5 air changes per hour, no recirculation) for 24-72 hours prior to installation. Acoustical ceiling panels shall not be stored with materials which have high emissions of VOCs or other contaminants (see section 3.01 below).

- Panels to be stored per manufacturer’s recommendations for allowable temperature and humidity range. Panels shall not be allowed to become damp.

PART 2 – PRODUCTS

2.01 MATERIALS

- Environmental Criteria:

- Recycled Content:

Acoustical panel ceiling systems shall contain recycled content material as follows:

- Mineral-wool and cellulose fiber based panels: a minimum of 50% (combined) post-industrial/post-consumer recycled content. If panels are specifically formulated for fire resistance (tested in UL-listed construction assemblies), a minimum of 35% (combined) post-industrial/post-consumer recycled content is required.

- Steel suspension grids: a minimum of 25% (combined) post-industrial/post-consumer recycled content.

The percentage of recycled content is based on the weight of the component materials.

PART 3 –  EXECUTION

3.01	INSTALLATION

- Where feasible, ceiling panels shall be installed after the installation of materials or finishes which have high short-term emissions of VOC’s, formaldehyde, particulates, or other air-borne compounds which may be adsorbed by or settle on the ceiling panels. Materials with high short-term emissions include, but are not limited to: adhesives, sealants and glazing compounds (specifically those with petrochemical vehicles or carriers); paint, wood preservatives, and finishes; control and/or expansion joint fillers; hard finishes requiring adhesive installation; gypsum board (with associated finish processes and products); and composite or engineered wood products with formaldehyde binders.

3.02	WASTE MANAGEMENT

- Identify ceiling panel manufacturer’s policy for collection or return of construction scrap, unused material, demolition scrap, and/or packaging material. Where feasible, institute demolition and construction waste separation and recycling to take advantage of manufacturer’s programs.

END OF SECTION 09510