# 10 2113 	PLASTIC TOILET   COMPARTMENTS AND RELATED  PRODUCTS

FINAL:  	Feb. 12, 2009

Note:  The following specification criteria have been assembled to promote the procurement of post-consumer/post-industrial recycled content in plastic toilet compartments and related solid plastic products. Additional considerations related to product emissions, product toxicity, or other High Performance building criteria are included where appropriate.

PART 1 - GENERAL

1.01  SUMMARY

- This section includes plastic toilet compartments which meet specified criteria for post-consumer and/or post-industrial recycled content.

- Additional related products include, but are not limited to, the following:

- Shower partitions

- Urinal screens

- Wall paneling/wainscotting

- Lavatories

  - REFERENCES / QUALITY ASSURANCE

(for recycled content and other High Performance building criteria)

- Recycled content:

- EPA Comprehensive Procurement Guidelines, www.epa.gov/cpg

1.03	SUBMISSION REQUIREMENTS

A	Manufacturer’s certification of recycled content per section 2.01 of this specification.

- Manufacturer’s maintenance and cleaning instructions.

- Manufacturer’s policy statement on plastic toilet compartment recycling programs.

PART 2 – PRODUCTS

2.01 MATERIALS

- Environmental Criteria:

- Recycled Content:

Plastic toilet compartments shall contain a minimum of 20% (combined) post-industrial/post-consumer recycled content with a minimum of 20% post-consumer recycled content. The percentage of recycled content is based on the weight of the component materials.

PART 3 –  EXECUTION

3.01	WASTE MANAGEMENT

- Identify manufacturer’s policy for collection or return of construction scrap, unused material, demolition scrap, and/or packaging material. Where feasible, institute demolition and construction waste separation and recycling to take advantage of manufacturer’s programs.

END OF SECTION 10170